## Slide 1
2014. 6. 17
CM Platform for Operating NPP

## Slide 2
Contents
Project Information
New built vs Operating NPP
Platform Modules for CM
Platform Architecture
DBD Taxonomy
Requirement Management Platform
Traceability Management Platform
Change Management Platform
Facility Configuration Information Platform
Physical Configuration
Demo

## Slide 3
Development of Configuration Management Platform for Operating NPP
Title
2013.10 ~ 2016.9 (3 years)
Period
NSE & KHNP
Organizations
Project Information
KETEP (Korea Institute of Energy Technology Evaluation and Planning)
Funding
Project Plan
2013
2014
2015
2016
Req. Analysis
Prototype
Req. Spec.
Platform Dev.
Test
Trial

## Slide 4
New-Built and Operating NPP
Item | New-Built | Operating
CM Model |  | 
Main Differences | Virtual Plant: Modeling 2-D and 3-D (dimensional), up to 4-D (time), 5-D (cost), and 6-D (material) The CM principles and practices are established and functional with Virtual Plant. Data-Centric CM Standards and Cooperation should be established among participated EPCs. Data-Centric should be used at operation time. | CM starts with confirming CM Equilibrium after information turnover. Main purpose is the change management to maintain CM Equilibrium of changing equipment. Document-Centric CM (including Electric files) Considering ready-made processes for equipment/material/quality management. Make old drawings intelligent in order to trace requirements and component in the drawings.
  Design
  Requirement
  What needs to be there
  Physical
  Configuration
  What is actually there
  Facility
  Configuration
  Information
  What we say
  is there
  Design
  Requirement
  What needs to be there
  Physical
  Configuration
  What is actually there
  Facility
  Configuration
  Information
  What we say
  is there
  Virtual Plant
  Data Model
Notes: The relationship of the information generated for new builds is sometimes called
Virtual Plant, which is defined as “a computer-based information model
environment formed by computer technology consisting of 2-D and 3-D
(dimensional), 4-D (time), 5-D (cost), and 6-D (material) modeling along with
data, databases, and electronic document sources.” Unlike the existing facilities,
Virtual Plant acknowledges that the physical configuration might not be in place,
but the CM principles and practices must be established and functional.

## Slide 5
Pictures
Physical Configuration
Facility Configuration Information
Platform Modules for CM
Information Management
Design Requirement Repository
Information
Traceability
Repository
Control Log
Repository
Data-centric Management
Data Warehouse
Document Repository
Workflow Management
Change Management
Process/2D Schematics
P&ID
Instrument Control
Schematics
3D
3D Drawings
Requirement Management
Design Bases Taxonomy
Requirement Control
Traceability Management
Dynamic Traceability
GUI Engine
Change
Management
Workflow(BPM) Engine
Change History
Design Requirement

## Slide 6
Legacy System
SAP
Workflow Management
Facility Configuration Management System
Data Warehouse
Document Repository
Workflow Management
Change Management
Process/2D Schematics
P&ID
Instrument Control
Schematics
3D
3D Drawings
Requirement, Information, Change, Traceability Management Platform
Information Management
Service Management
Security Service
Design Requirement Repository
Information
Traceability
Repository
Requirement Management
Design Bases Taxonomy
Requirement Control
Documents Management
Integrated Configuration Management Platform
Control Log
Repository
Engineering Data Sync. Channel
SAP Sync. Channel
Policy Service
Facility
Mapper
Web Service
Material Data
2D Drawing
Requirement View
Old Data
Data-centric Management
Authorization Service
Traceability Management
Dynamic Traceability
GUI Engine
Change
Management
Workflow(BPM) Engine
Change History
Traceability View
Workflow/Change View
Platform Architecture
Platform Architecture

## Slide 7
DBD TAXONOMY
Reference: EPRI TR; 1022684; April 2011

## Slide 8
System
Taxonomy
DBD
Requirement Management
Requirement Management Platform
Ultimate Capability
Design Margin
Analyzed Design Limit
Operating Limit
Unanalyzed margin
Range of Normal Operation
Margin Configuration Management
Operation Margin

## Slide 9
System
Traceability Management
Change Management
Search
Requirement Management
계측계통
구조물계통
일차보조건물계통
발전소보호계통
공학적안전설비작동계통
보조급수계통
1차측기기냉각수계통
주급수계통원자로냉각재계통
안전주입계통 및 정지냉각계통
비상디젤발전기계통
사용후연료저장조 냉각/정화계통
유체계통
Taxonomy
DBD Management
Requirement Management Platform
Fluid System
Instrumentation System
Structure system
Primary Auxiliary Building
Plant protection system
Engineered Safety Feature Actuation System
Auxiliary Feedwater System
Feedwater System
Reactor Coolant System
Safety Injection System
Shutdown Cooling System
Emergency Diesel Generator System
Spent Fuel Pool Cooling and Cleanup System

## Slide 10
Design
Requirement
Design Base Specification
System, Structure, Component Specification
Design
Parameter
Supporting
Design
Information
Supporting Operating Information
Requirement Traceability Platform
Taxonomy-based Traceability (EPRI PIM View)

## Slide 11
Traceability Management Platform
Report View
Radial Diagram View
Taxonomy View
Tree View

## Slide 12
CM001
Evaluate Identified
Problem or Desired
Change
Change design
requirements
Change physical
requirements
Change facility
configuration
information
Do nothing more
CM002
Design Requirements
Change Processes
CM003
Physical Configuration
Change Authorization
Processes
CM004
Facility Configuration
Information Change Processes
Yes
Yes
Yes
No
No
No
CM Equilibrium
Change Management Platform
AP-929

## Slide 13
Change Process
(Company Specific)
+
X
+
X
BPM Engine
Portal
Work Place
Monitoring
Reports
Dashboard
· · ·
Change Management Platform

## Slide 14
Equipment
Procedure
P&ID(dgn)
Intelligent Data
Intelligence
Specification
Calculation
FSAR
Material
Tag Mapping
FCI Platform
Facility Configuration Information Platform
Expected
Actual
Intelligent Documents
Procedure, etc.
Equipment
P&ID(dgn)
Material BOM
Legacy System

## Slide 15
Physical Configuration
Panorama View
Ex) Fossil Plant provided by POMIT Inc.

## Slide 16
Demo