## Slide 1: Pilot Component Design Basis Inspection (CDBI) and Equipment Qualification (EQ) Program Inspection Feedback
Configuration Management Benchmarking Group (CMBG)
Palm Beach Gardens, FL
June 7, 2016
Glen E. Schinzel
STPNOC, Design Engineering
geschinzel@stpegs.com

## Slide 2: CDBI Background
Purpose of the NRC Component Design Basis Inspection (CDBI) is to:
  Verify that plant components are maintained within their design basis
  Monitor the capability of the selected components and operator actions to perform their design basis functions
Inspection Scope
  Typically eleven to sixteen components are selected
  One to three components are typically associated with containment-related SSCs which are considered for Large Early Release Frequency, and
  Three to six components associated with issues identified through the operating experience feedback process

## Slide 3: CDBI Insights
The CDBI is a baseline inspection in the NRC Regulatory Oversight Process (ROP)
The inspection is nominally performed on a triennial frequency
The NRC previously estimated inspection hours at about:
  475 hours (single unit sites)
  500 hours (multi-unit sites)
  In actuality, many sites experienced many more hours of inspection
NRC Inspection Fees
  Industry survey indicated NRC Inspection fees averaged $361,000 and ranged up to $500,000

## Slide 4: CDBI Insights
NRC inspection team is typically comprised of 6 inspectors (including contractors)
Licensee costs for pre-inspection preparation, direct inspection support and post-inspection activities ranged up to $650,000 excluding contractor costs

## Slide 5: Baseline CDBI Inspection Schedule (typical)
Initial information requests
On-site Visit (Bagman Trip)
In-office preparations (2nd week may be added)
Week 1: Onsite inspection of selected samples
Week 2: In-office inspection
Week 3: Onsite inspection
Week 4: In-office inspection
Week 5: Onsite inspection
Documentation/Report Development

## Slide 6: Pilot Approach
Beginning in 2014, industry and NRC engaged in dialog on how to improve the effectiveness of current CDBIs
Due to industry concerns with the cost and scope of CDBIs, the Regulatory Issues Working Group (RIWG) along with the Nuclear Energy Institute (NEI) recommended changes to the CDBI program
As a result of industry and NRC internal interest, a new CDBI pilot program (IP 71111.21T) was developed
 | IP 71111.21 (Baseline) Components | IP 71111.21T (Pilot) Components
Components | 11 to 16 | 8 to 12
Containment SSCs | 1 to 3 | 1 to 2
Operating Experience | 3 to 6 | 1 to 3
Level of Effort | 15 to 25 | 10 to 17

## Slide 7: Pilot Approach
CDBI Inspection
  Reduce the sample size and amount of inspection time on components
  Reduce the impact on licensees while still providing the inspection value
  2 pilot inspections from each region
  Take lessons learned from the pilots and develop a revised CDBI inspection approach to be implemented at all licensee starting calendar year 2017
Added an engineering program inspection into the process
    Pilot inspection of the Equipment Qualification (EQ) program

## Slide 8: Pilot CDBIs/Program Inspections
Pilot inspections held at:
NRC Region | Plants
I | Calvert Cliffs – CDBI and EQ Inspection Complete Fitzpatrick – CDBI and EQ Inspection Complete
II | Browns Ferry – CDBI and EQ Inspection Complete St. Lucie – CDBI and EQ Inspection Complete
III | D.C. Cook – CDBI and EQ Inspection Complete Dresden – CDBI Complete; EQ Inspection on 06/20-24
IV | South Texas Project – CDBI and EQ Inspection Complete Columbia Generating Station – EQ Inspection Complete; CDBI on 06/06-24

## Slide 9: Pilot CDBI Inspections
Initial information requests
Onsite Visit “Bagman Trip”
In-office preparations
Week 1: Onsite inspection of selected samples
Week 2: In-office inspection
Week 3: Onsite inspection
Documentation/Report development

## Slide 10: Pilot EQ Program Inspections
Initial information requests
Onsite Visit “Bagman Trip”
In-office preparations
Onsite inspection of selected samples (one week)
Documentation/Report development

## Slide 11: STP Experience/Feedback
Pilot CDBI scope mimicked the 5-week CDBI inspection scope
Component scoping included some systems/sub-systems
NRC information request was extensive and similar to past CDBI requests
Additional information requests from NRC were provided late
Inspection activities began on the first day of the Prep Week

## Slide 12: STP Experience/Feedback
Scope and rigor of the inspection was challenging
Inspection activities continued during the ‘Off’ Week
More documented NRC requests than previous 5-week inspection
Potential findings were communicated late in the process
Inspection activities continued for several weeks post-Exit
Initial exit was on 02/11; a telephone re-Exit occurred on 03/09

## Slide 13: STP Experience/Feedback
EQ Program Inspection:
  Initial information request mimicked or exceeded the CDBI initial information request
  EQ Bag Trip occurred during last week of the CDBI
  Some challenges with inspector knowledge of this new inspection scope

## Slide 14: Industry Overall Experience/Feedback
The overall industry pilot experience wasn’t as bad as STP’s
General feedback is that the pilot approach shows promise:
  Reduced inspection ‘footprint’ and the ‘levelization’ of inspection scope provides benefit
  However, the aggregate impact of the design and program inspections has resulted in an increased burden on plant resources as compared to the original baseline CDBI
  Modest changes to the pilot approach can successfully address this concern

## Slide 15: Industry Overall Experience/Feedback
Overall positives:
  Adherence to inspection procedures and Team Lead performance
  Ability to complete deep dives into complex issues within the inspection timeframe
Opportunities to improve:
  Sample size
  Sample selection
  Inspection focus area
  Data requests
  Inspection scheduling

## Slide 16: Adjustments for Success
Reduce CDBI sample size to 7-10 components
Select samples at the component level; eliminate systems and groupings of components as a single sample
Minimize re-inspection of components
Refocus on licensee ability to maintain design and design margins over time (reduce focus on challenging the original design)
Re-examine the need for extensive data requests
Eliminate schedule overlap with CDBI and Program inspections

## Slide 17: Next Steps
Industry/NRC meeting was held on May 13 to discuss the to-date feedback
Industry roll-up of pilot program results will occur in the June/July timeframe
NRC pilot CDBI/Program review meeting scheduled for July 19

## Slide 18: Going-Forward Actions
NEI to create an industry focus group to pursue further changes to the CDBI process:
  Improve CDBI sample selection criteria
  Focus the CDBI on design control
  Streamline/focus document requests and data collection
  (Long-term consideration) Develop strategy to eliminate the triennial Fire Protection inspection by including fire risk components within the CDBI