## Slide 1: 10CFR50.69 – Approaches/Impacts on Configuration Management Configuration Management Benchmarking Group Summer 2018 Conference Chattanooga, TN Glen E. Schinzel STPNOC, Design Engineering geschinzel@stpegs.com

## Slide 2: Overview
10CFR50.69 offers a significant strategic opportunity for current operating stations
Enhanced safety benefits
Substantial economic savings available
Benefits available for PWRs / BWRs
Requires a commitment of senior leadership and staff
Investment in the future viability of your station
Considerations for managing CM impacts must be factored in

## Slide 3: 10CFR50.69 Background
10CFR50.69 is an approved regulatory rule that allows safety-related SSCs determined to have Low safety significance to be removed from the scope of a number of regulatory requirements
  SSCs must be categorized using an NRC-approved methodology
50.69 is not a new rule
  The proto-type was piloted by STP beginning in 2001
  Rule published on 11/22/04

## Slide 4: 10CFR50.69 Background
10CFR50.69 is a scoping rule in that regulatory requirements are NOT eliminated, but the scope of components subject to these regulatory requirements is changed
Licensees can choose the degree and timing of treatment changes – can categorize 1, 2, 5, 12, etc. systems
Adoption of 10CFR50.69 is VOLUNTARY
Recent economic challenges within the industry has renewed and broadened interest to pursue 50.69
  Delivering the Nuclear Promise
  Efficiency Bulletins were issued to encourage use
  A number of licensees have submitted (or will submit) a License Amendment to adopt 50.69

## Slide 5: Treatment Changes
Safety Related
High Safety Significant
Non Safety Related
High Safety
Significant
Non Safety Related
Low Safety
Significant
Safety Related
Low Safety Significant
RISC 1
RISC 2
RISC 3
RISC 4
RISC = Risk Informed Safety Class
Confirm treatment for beyond design basis functions
Confirm treatment adequate for risk-significant attributes
No additional treatment necessary
Apply Owner-Controlled Alternate Treatment
Notes: RISC-1 or RISC-4 SSCs: no change to treatment occurs
RISC-2 SSCs: an assessment is performed of current applied industrial practices
  Licensee to determine if additional treatments should be applied
RISC-3 SSCs: these components are largely removed from the scope of regulatory special treatment requirements
  SSCs remain classified as safety-related
  Applied treatments largely mirror robust industrial practices – must have reasonable confidence that design functional requirements still satisfied

## Slide 6: Regulatory Rules Affected by 50.69
  Maintenance Rule
  [10 CFR 50.65]
  Environmental Qualification
  [10 CFR 50.49]
  Seismic Qualification [Portions of Appendix A to 10 CFR Part 100]
  ASME XI repair & replacements, applicable portions, with limitations
  [10 CFR 50.55a(g)]
  Applicable Portions of IEEE standards
  [10 CFR 50.55a(h)]
In-service Testing [10 CFR 50.55a(f)]
In-service Inspection
[10 CFR 50.55a(g)]
Local Leak Rate Testing
[10 CFR 50 Appendix J]
Quality Requirements
[10 CFR 50 Appendix B]
Deficiency Reporting
[10 CFR Part 21]
Event Reporting [10 CFR 50.55(e)]
Notification Requirements
[10 CFR 50.72, 50.73]

## Slide 7: Some CM Considerations for 50.69
50.69 does not change the design of the Station:
  The safety classification of the SSC does not change
However:
  Alternative industrial parts/SSCs can be installed in RISC-3 applications (no change to safety classification)
  Updates to MEL may be needed as parts are changed out
  May involve updates to specifications, designs, drawings, etc.
  Will result in changes to how RISC-3 SSCs are treated
Notes: MOVs - test frequency extensions implemented
AOVs/SOVs - test frequency extensions implemented
Check Valves - test frequency extensions implemented - performing needed testing to satisfy basis of reasonable confidence
Relief Valves - continuing to test on a 10 year frequency, but scope expansion not required if lift test failure noted (CR written)
Pumps - test frequency extensions implemented

## Slide 8: Categorization vs. Treatment
The categorization process is separate from treatment adjustments
  Involves different teams of personnel
Only categorized systems/components are available to have alternate treatments applied
All SSCs within a selected system must be categorized
50.69 eliminates many special treatment requirements for RISC-3 applications – however, 50.69 also defines requirements to be applied to RISC-3 applications and for obtaining "reasonable confidence" in performance of design basis function(s)
Notes: MOVs - test frequency extensions implemented
AOVs/SOVs - test frequency extensions implemented
Check Valves - test frequency extensions implemented - performing needed testing to satisfy basis of reasonable confidence
Relief Valves - continuing to test on a 10 year frequency, but scope expansion not required if lift test failure noted (CR written)
Pumps - test frequency extensions implemented

## Slide 9: Keys to Successful Implementation
Sponsorship from senior leaders is essential
Strategically determine up-front what you want to accomplish with 50.69
  Verbalize clearly and translate into an effective Business Case
  Understand the scope and pace you wish to pursue
  Business Case needs to lay out a realistic schedule with supporting resources (personnel and budget)
Engage affected organizations
  Ensure understanding and the sound basis for process changes

## Slide 10: Keys to Successful Implementation
Dedicate resources to support implementation
  A strong project manager is needed
  Don’t rely on individual organizations ‘getting it’ and self-implementing the allowances
Establish milestones and indicators to reflect progress
  Establish clear means of defining ‘savings’
  Capture soft and hard dollar savings
Collaborate with others
  PWROG/BWROG 50.69 Alternate Treatment Teams have been established
  Certain implementation details are being worked out
  Don’t ‘go it alone’ – actively make use of industry expertise

## Slide 11: Breakout Material

## Slide 12: In-Service Testing (IST) Overview
Per 50.69, the scope of SSCs subject to In-service Testing (IST) requirements could be reduced for RISC-3 SSCs:
  MOVs, AOVs/SOVs, Check Valves, Relief Valves, Pumps
For SSCs removed from scope, it is required that:
  Periodic inspection and testing activities be conducted to determine that these SSCs will remain capable of performing their safety-related functions under design-basis conditions
Notes: MOVs - test frequency extensions implemented
AOVs/SOVs - test frequency extensions implemented
Check Valves - test frequency extensions implemented - performing needed testing to satisfy basis of reasonable confidence
Relief Valves - continuing to test on a 10 year frequency, but scope expansion not required if lift test failure noted (CR written)
Pumps - test frequency extensions implemented

## Slide 13: In-Service Testing Program (Example)
For STP, RISC-3 SSCs available to be removed from IST scope totaled 251 valves and 8 pumps
  STP initially focused on frequency extensions for RISC-3 SSCs
  STP performed assessments on each affected test group
  Basis for test group frequency extensions were documented on a formal engineering evaluation – approved and controlled
  Periodic test data collection/trending of results still occurs
No increased failure rates noted based on test frequency changes
Notes: MOVs - test frequency extensions implemented
AOVs/SOVs - test frequency extensions implemented
Check Valves - test frequency extensions implemented - performing needed testing to satisfy basis of reasonable confidence
Relief Valves - continuing to test on a 10 year frequency, but scope expansion not required if lift test failure noted (CR written)
Pumps - test frequency extensions implemented

## Slide 14: In-Service Testing Overview & Status
With full implementation, differences in treatment for RISC-3 SSCs removed from scope vs. RISC-1 SSCs include:
  test frequencies extended based on past performances and reasonable confidence for successful future performance
  testing occurs under a Preventive Maintenance (PM) task vs a Surveillance Test (ST)
  trending still validates expected successful operation until the next test performance
  if a test fails to meet expected criteria, a Condition Report will be written rather than documenting a failed surveillance test

## Slide 15: Regulatory Inservice Testing vs. RI-IST
Licensees can still pursue a Risk-Informed IST (RI-IST) program in addition to 50.69
Graded approach can be applied to those SSCs remaining within the regulatory IST scope
At STP, for those SSCs still within the regulatory IST scope (RISC-1), the additional opportunity includes:
  178 valves and 7 pumps that could be determined to be RI-IST Low and could have their frequency of testing extended

## Slide 16: Local Leak-rate Testing Overview
Per 50.69, Type B and Type C Local Leak Rate Testing (LLRT) is not required for safety-related valves determined to be RISC-3 and that satisfy one or more of the following criteria:
  Containment penetrations are 1” in size or less, or are continuously pressurized (Type B)
  valve is open with mass flow during accident scenarios
  valve is normally closed in a closed water-filled system
  valve is in a closed piping system which has a crush pressure greater than that of Containment and is not connected to the RCS
  the valve is 1” in size or smaller

## Slide 17: Local Leak-rate Testing Implementation (Example)
LLRT Program procedure modified to reflect scope adjustment
Each penetration which contained RISC-3 valves was evaluated against scoping criteria
Evaluation results documented on a formal engineering evaluation – approved and controlled
For valves that satisfy scoping criteria, annotated that LLRTs are no longer required in the Surveillance database
Training provided to Performance Techs and Operations

## Slide 18: STP Local Leak-rate Testing Implementation
43 penetrations were removed from regulatory-required Type C LLRT testing – scope reduced by 57% - also applied insights to Integrated Leak-Rate Test in Unit 2
LLRTs may still be performed if deemed prudent to perform the test
LLRT STs have not been deleted - frequency of performance changed to an Inactive status
No substantive performance degradation has been noted to date due to reduced scope of LLRT testing

## Slide 19: Parts Procurement Approach at STP
RISC-3 replacement parts are assessed on an as-needed basis - no large-scale procurement approach pursued
Evaluations are initiated by Procurement personnel and forwarded to Engineering for evaluation
  Procurement personnel provide the initial screening for potential to exercise the RISC-3 allowances
  If industrial part is available and appears economically beneficial, a Condition Report is generated for Engineering to evaluate acceptability of the proposed industrial part

## Slide 20: STP Parts Procurement Overview
Examples of industrial parts that have been installed in RISC-3 applications:
  Spent Fuel Pool Heat Exchanger discharge valve flow guide
  Radiation Monitor sample pumps
  Safety-related vent and drain valves
  HVAC analog-to-digital flow controller change out
  Capacitors on computer card rebuilds
No adverse performance trends noted to date for industrial parts in RISC-3 applications
No adverse warehousing issues noted to date with RISC-3 industrial parts
Notes: No adverse warehousing issues noted to date with the receipt/handling of RISC-3 industrial parts

## Slide 21: Insights on STP Parts Procurement
Available safety-related stock in the warehouse must be depleted before actual use of commercial replacement parts are considered
  Delay in actual recognition of parts savings
  Could assess warehousing approach for RISC-3 SSCs
Some potential commercial part replacements are not economically viable - in these cases, safety-related parts continue to be procured and installed
Cultural issues are a challenge for Engineering, Procurement, and Maintenance organizations

## Slide 22: STP Maintenance Rule Approach
RISC-3 SSCs can be removed from the scope of 10CFR 50.65 (but not (a)(4))
For each MR-scoped system where the entire system is RISC-3 or RISC-4, the system is removed from MR scoping
Some significant MRFF contributors have been removed from scope
  Radiation Monitoring, Emergency DC Lighting
In addition, STP has made the business decision that if a system is plant generation significant, it will be administratively tracked against the Maintenance Rule
  failures not counted as MRFFs
Notes:   RISC-3 SSCs can be removed from the scope of 10CFR 50.65
    does not apply to (a)(4) aspects
  required to monitor performance on a plant/system/train level as appropriate
  components affecting HSS functions will be monitored and assessed in accordance with plant, system, and/or train performance criteria
Maintenance Rule (MR) Basis Document to be revised to reflect the scope change allowances

## Slide 23: Environmental Qualification Overview
Per 50.69, the scope of RISC-3 SSCs subjected to 10CFR 50.49 requirements can be reduced
  Qualification requirements imposed under 50.49 not required
  Design functional requirements still need to be satisfied; however, the rigor required to meet this is reduced (i.e., qualification testing, test report generation/retention, etc.)
  Can take credit for current qualified conditions
  Qualified life extensions much more straight-forward

## Slide 24: STP Environmental Qualification Approach
STP’s initial EQ Program included 2,533 SSCs:
  1931 of these SSCs were determined to be RISC-3
  Total number of SSCs in EQ Program is now 602 (a reduction of 76%)
Implementation benefits take a number of forms:
  Qualified life extensions using formal engineering evaluation
  Commercial parts procurements
  Reduction in testing rigor
  Reduction in test report processing

## Slide 25: Tool-Pouch Maintenance Overview
Tool-Pouch Maintenance (TPM) is a means of resolving simple deficiencies which are within the skill sets of the available craftsmen
  no documented work planning is needed
  no work implementation scheduling is needed
TPM process is procedurally controlled
TPM process permits minor deficiencies on RISC-3 SSCs to be corrected in an expedited fashion
  safety benefit to restore RISC-3 SSCs to a reliable, fully-functional condition

## Slide 26: Tool-Pouch Maintenance Overview, Status
Procedures modified to permit use of TPM on RISC-3 SSCs
  TPM previously was only permitted on non-safety related SSCs
  A Condition Report is still generated to document the RISC-3 SSC deficiency
  The craftsman documents the correction electronically in the CAP database - no paperwork generated or vaulted
  PMTs are still performed, if required, to validate that the SSC is satisfying its design functional requirement
Since revision of the TPM procedures, no adverse SSC performance trends have been attributed to TPM implementation

## Slide 27: Additional Uses of Categorization Insights
Categorization insights afford many opportunities to enhance station decision-making – other uses include:
  Strategically determining which design changes should be prioritized for safety enhancements
  Preventive Maintenance optimization efforts to revise scopes and frequencies of performance
  Used as a ‘risk-informed evaluation process’ to establish what constitutes ‘covered work’ within the NRC Work-Hour Rule
  System Engineering Health Report focus
  Corrective Action Program apparent cause and root cause evaluation criteria

## Slide 28: STP Implementation Overview
STP chose to pursue a cautious, deliberate implementation approach
Based on stakeholder support and available baseline resources, STP pursued program and process changes in the following areas first:
  IST (10CFR 50.55a(f))
  LLRT (Appendix J)
  Parts procurement (Appendix B, 10CFR 50.49)
  Tool-Pouch Maintenance (Appendix B)
  Maintenance Rule (10CFR 50.65)

## Slide 29: STP Implementation Process
Periodic feedback to the IDP is important to ensure that categorization results remain well founded and defensible
  A periodic assessment is done of all categorized systems once every three years – looks at overall equipment performance changes (operating experience trends)
  PRA Model updates are communicated to the IDP – main driver for categorization changes
  System Engineer feedback is provided to overview changes to system health
  Feedback is gathered from Operations, Licensing, and Quality for changes to procedures and processes that might affect categorization outcomes

## Slide 30: Keys to Successful Implementation
View implementation as a key ingredient to station survival
  50.69 definitely reduces regulatory burden
  Enhances nuclear safety while reducing costs
  Permits more effective ways of accomplishing change
  Adds efficiency into well-established processes