## Slide 1
Development of Advanced 3D Models for Cyber Plant
in Saeul NPP Units 3&4 and Practical Usage
2023. 06. 28
DAEYOUNG JEONG
(KEPCO E&C, South Korea)

## Slide 2
TABLE OF CONTENTS
2
Management Procedure
1
Introduction
3
Enhancement Plan
4
Validation Process
5
Practical Usage of Cyber Plant
6
Conclusion

## Slide 3
Introduction

## Slide 4
Purpose of Cyber Plant
Existing NPP
Cyber Plant
01
Introduction
Effective Operation
Preventative
Maintenance
It is required to meet the new restricted regulation for nuclear power plant operation
It is needed to establish Cyber Plant to assure the safety of nuclear power plant operation
Cyber plant is 3D digitalization of existing nuclear power plant
It can be used for Training, Effective Operation and Preventative Maintenance
3D Digitalization
Training System
VR System

## Slide 5
01
Introduction
Status of SN 3&4 Cyber Plant Project
KEPCO E&C Cyber Plant Development
Management Procedure
Enhancement Plan
Validation Process
Establishment of New 3D Models
Standardization of Commonly used 3D Models
Reconstructing Piping Joint Shape
Integration and Advanvement
Consistency Check related with Tag Numbering Sytem of Project Participants
Application of Colors to Applicable Components
Conversion and Transfer 3D Models file to Cyber Plant
KHNP Application of Cyber Plant Technology
Information HUB
Device Disassemble on Decommissioning Phase
VR Application on Operation Phase
Model File Numbering System
Components Numbering System
Components Propertites
Color of 3D Models
Existing
3D Models
New
3D Models

## Slide 6
01
Introduction
Status of SN 3&4 Cyber Plant Project
KEPCO E&C Cyber Plant Development
Management Procedure
Enhancement Plan
Validation Process
Establishment of New 3D Models
Standardization of Commonly used 3D Models
Reconstructing Piping Joint Shape
Integration and Advanvement
Consistency Check related with Tag Nubering Sytem of Project Participants
Application of Colors to Applicable Components
Conversion and Transfer 3D Models file to Cyber Plant
KHNP Application of Cyber Plant Technology
Information HUB
Device Disassemble on Decommissioning Phase
VR Application on Operation Phase
Model File Numbering System
Components Numbering System
Components Propertites
Color of 3D Models
Existing
3D Models
New
3D Models

## Slide 7
Management Procedure

## Slide 8
02
Management Procedure
Management Procedure Concept
3D Integrated Models
Model file Numbering System
Advanced 3D Models for cyber plant
Color of 3D Models
Components Numbering System
Components Properties
Consistency
Reality
Compatibility
Availability to manage Advanced 3D Models for cyber plant

## Slide 9
02
Management Procedure
Model file numbering system
Index | SN 3&4 | Cyber Plant
File Type | M : 3D Model | V : Cyber Model
Unit No. | Unit number | Unit number
PBS No. | Physical breakdown structure number | Physical breakdown structure number
Model Type | Components Type | Components Type
Serial No. | Area No. (ex. M-3-321-A-010-00) | Area No. + Subsystem No. (ex. V-3-321-A-01B-00)
Revision No. | File revision number | File revision number
O-O-OOO-O-OOO-OO
Unit No.
PBS No.
Revision No.
V-3-321-A-01B-00 (sample)
File Type
Model Type
Serial No.
Discipline | Subsystem No. | Description
Civil | B | Anchor Bolt
 | C | Conduit Opening
 | L | Sleeve
 | S | Sheath
 | T | Tendon
Architecture | D | Door

## Slide 10
SN 3&4
Cyber Plant
02
Management Procedure
Components numbering system
9-691-V-4519
9-325-P191-181(Pan DWG.)
9-691-V-4519
3-691-V-4519
4-691-V-4519
For DWG.

## Slide 11
02
Management Procedure
Components properties
Task
- Identify the information of each components for operation
- Define the properties of common and specific data
Scope (Sample)
Common Data |  | Specific Data | 
Component No. | 3/4-535-V-0013 | Flow rate (Lbs/Hr) | 1,300
Function | Containment ISO. | Pressure(psig) | 60
Classification | Safety Related | Temperature(°F) | 300
Specification No. | 9-145-P206A | Valve type | Gate
Manufacture | SAMSHIN | Diameter(in) | 6
DWG No. | 9-P206A-DG-A01-05 | End Type | Buttweld
Active or Passive | Active | Actuator Type | MOV
3/4-535-V-0013

## Slide 12
02
Management Procedure
Color of 3D Models
SN 3&4
Cyber Plant
Software
Piping
Components

## Slide 13
02
Management Procedure
Color of 3D Models
Piping
- Classify the color of piping with respect to the fluid of system in accordance with
design specification
- Color Band (Sample)
Fluid Type | System | Color name | Color
Demineralized Water, Fresh Water | CC, CD, CP, CT, AX, DM, DG-Water | Light Blue | 
Radioactive, Radwaste | DE, FC, WV, WX, WY | Dark Red | 
Fire Fighting (CO2 , Haloge, Water) | CO, FP | Red | 
HVAC vent and drain etc. | VC, VD, VE, VF, VG, VK, VO, VP, VQ | Grey | 
Steam and Hot Water | RC, SI, CS , IW | Yellow | 
< Color bands for Piping in design specification >
The color applied to pipe identification depends on a color chart
for content recognition.

## Slide 14
02
Management Procedure
Color of 3D Models
Components
- Classify the color of components with respect to applicable purchase specification
- Color Band (Sample)
< Requirement of color in purchase specification >
Component | Color
Condensate Pumps | Grey
Feedwater Booster Pumps | Grey
Spec. No. | Component Type | Description | System | Color
9-132-M210 | PP | Circulating Water Screen Wash Pump | SW, CL | 
9-133-N204 | HX | Containment Heat Exchanger | CS, CC, FC | 
9-531-M208 | PP | Feedwater Booster Pumps | CD, FW, WT | 
9-596-M224 | FT | Filter | IA | 
 | LP | Air Compressors Local Control Panel | IA | 
9-691-M258 | VV | Relief Valve for Diesel-Driven Fire Pump | FP | 

## Slide 15
02
Management Procedure
Color of 3D Models
Piping
Components (Sample : Feedwater Booster Pump)
SN 3&4 NPP
Cyber Plant
SN 3&4 NPP
Cyber Plant

## Slide 16
Enhancement Plan

## Slide 17
03
Enhancement Plan
Purpose
Advanced 3D Models are required for cyber plant to utilize VR system with reality
By enhancement plan, it is available to establish advanced 3D Models
Work flow
Integrated 3D Models
Advanced 3D Models
New 3D Models
Existing 3D Models
in SN 3&4
Integration
Advancement

## Slide 18
03
Enhancement Plan
No. | Department | New 3D Models | Quantity | Remark
1 | Architecture | Door & Louver | 1,705 | 
2 | Civil | Anchor Bolt Tendon & Sheath Sleeve | 32,310 | 
3 | Electric | Lighting & Fire Detectors | 12,937 | 
4 | I&C | Instrument | 22,012 | 
5 | Piping | Plumbing Pipe & Fixture Weld Joint Configuration | 793,900 | 
6 | Common | Design Base Drawing RCS Piping Welding | 160 | 
Total |  |  | 863,024 | 
New 3D Models
Task
- Development of new 3D Models which should be developed additionally for
advanced 3d models
- New 3D Models include door, louver, anchor bolt, etc.
Scope (Sample)

## Slide 19
No. | Title | Type
1 | General Requirement | -
2 | Bracket | 37
3 | Flow | 11
4 | HVAC | 9
5 | Level | 17
6 | Pressure | 8
7 | Rack & Support | 15
8 | Sample | 8
9 | Temperature | 11
10 | Pneumatic | 5
11 | Fabrication | 10
Total |  | 131
Instrument List
Instrument Installation Drawing
Supplier Drawing
Site Configuration
3D Modeling Cell
New 3D Models
03
Enhancement Plan
Work Flow for New 3D Models

## Slide 20
03
Enhancement Plan
New 3D Models
Component | Type | DWG. | Standardization
Lightning Fixture | HM-A2, CM, LFH-A |  | 
Fire Detector | Heat Detector, Flame Detector |  | 
Instrument | LIT, TS |  | 
Standardization
- Standardization of commonly used components

## Slide 21
03
Enhancement Plan
New 3D Models
Result of Standardization

## Slide 22
03
Enhancement Plan
Reconstruction
- Difficulty to figure out the weld point of existing piping joint shape
- Detailing the piping joint shape for advanced 3D Models
SN 3&4 NPP
Reconstruction by DWG
Cyber Plant
New 3D Models

## Slide 23
03
Enhancement Plan
3D Models Integration & Advancement
Task
- Integration of the existing models and new models
- Check the interference among 3D Models
- Review and remove duplicate objects
- Entity the attributes of integrated 3D Models
+
Review integrated 3D Models interference
Integrated 3D Models
SN 3&4 3D Models
New 3D Models
Remove duplicate objects
Entity the attributes
Advanced 3D Models

## Slide 24
Validation Process

## Slide 25
04
Validation Process
3D Models Validation Process
Task
- Comparison between KHNP and KEPCO E&C database
- Application of colors to 3D Models in accordance with management procedures
- Conversion of 3D Model file format for application of the operation program
Comparison between KHNP and KEPCO E&C database
Application of colors to advanved 3D Models
Conversion of Format for Operating Program

## Slide 26
Cyber Plant Practical Usage

## Slide 27
05
Cyber plant practical usage
3D Model Advancement
Utilizing Cyber Plant 3D Model
MCR Realization
Detailing Site Facility and Layout Model
Interlocking with Simulator
Analysis and Verify Interlocking Data/Attributes
Develop Interlocking System
VR System
Produce MMI Display
Build Symbols and Attributes
Function of VR Interaction
User Interface
VR Training Integrated Management System
VR Operation Procedure Training System
Scenario
Data Collecting
Verify Operation Procedure
Generate Operating Scenario based on VR
Procedure
RCS Fill and Vent
Severe Accident Management Guide
Abnormal(Loss of Condenser Vacuum and Operation in Plant Fire)

## Slide 28
Conclusion

## Slide 29
06
Conclusion
SN 3,4
3D MODEL
NEW 3D
MODEL
INTEGRATED 3D MODEL
VR 3D MODEL
Management
3D Models Enhancement
3D Models Validation
Cyber Plant Appication
3D Models Data Transformation
Conversion of Format for Operating Program
Piping Joint Reconstruction
KEPCO E&C
KHNP
CLASH CHECK
Comparison between KHNP and A/E components data
SN34 Reflection

## Slide 30
Thank You